## Slide 1
FlowArm PLTW Programming
Introduction
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 2: Help Available in Hardware and Software Manuals
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing
Notes: The Lynxmotion hardware and software online manuals can be accessed directly from the FlowArm PLTW interface through the link shown.

## Slide 3: User Interface Information
Click to show icon information
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 4: FlowArm PLTW Emergency Stop
Emergency Stop or E-Stop
stops all servo motion and communication.
Select again to resume operation.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 5: Robotic Arm Start Up Using a USB Cable and SSC-32U
Step 1. Connect the robot to a computer via USB cable. Wait for the Windows drivers to load. Note that this takes longer the first time.
Step 2. Connect the AC power adapter cable to the robot.
Step 3. Move the single switch to the on position.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 6: Robotic Arm Start Up Using a USB Cable and SSC-32U
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing
Step 4. Open the FlowArm PLTW software.
Step 5. Select the Bluetooth Button.
Refer to Lesson 3.3 Lynxmotion Robotic Arm.

## Slide 7: FlowArm PLTW Sequencer
Sequence
  Pattern consisting of multiple frames
Sequencer
  Allows a pattern of robotic arm positions called frames to be recorded
  Allows a pattern of frames to be played so a robotic arm repeats actions
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 8: General Sequence Outline
Use these steps as a guide for moving objects.
Begin at a start position with gripper open.
Move the hand to a position directly above an object.
Move the hand to the object.
Close the gripper.
Lift the object up.
Move the object to a position above the drop-off position.
Set the object down where you want it.
Open the gripper.
Return to a position above the object.
Return to home position.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 9: Sequencer General Steps
Use these steps to develop a sequence.
Save the current sequence.
Position the robot in a “home” position.
Record the position.
Click the button to add a position.
Move the arm to desired position.
Record the position.
Repeat steps 4–6 to complete sequence.
Click individual steps to verify positions.
Rewind and play the entire sequence from the first step.
Save the current sequence.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 10: Sequencer General Steps
Step 1: Save the selected pattern.
Enter a meaningful file name and select Save.
Note that the words sequence and pattern are interchangeable.
WARNING!
Unless the pattern is saved, all changes will be lost when you close the FlowArm PLTW software
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 11: Sequencer General Steps
Step 3: Record the current position in the selected frame.
The current position of every servo will be recorded.
Step 2: Move the robot to a start position using a preferred arm movement method.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 12: Sequencer General Steps
Step 5: Move the robot to a start position using a preferred arm movement method.
Note to remove a frame select it in the Sequencer and then select the Delete Frame button.
Step 4: Add a frame.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 13: Sequencer General Steps
Step 8: Click on each frame to verify the correct position.
Adjust the time duration of each frame by dragging the end of the frame.
Step 7: Repeat steps 4–6 until the pattern is completed.
Step 6: Record the current position in the selected frame.
WARNING!
A step duration must allow an arm to physically complete the step. If the duration is too short, then the step might be skipped or the arm does not reach the correct target.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 14: Sequencer General Steps
Step 10: Save the current sequence.
Step 9: Rewind the pattern to the beginning and play the sequence.
Make necessary changes to the sequence.
Stop; vary playback speed or loop
Recording.
WARNING!
Unless you save the pattern all changes will be lost when you close FlowArm PLTW software
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 15: Sequencer Tips
Sequence options: pause, remove gaps, and reverse.
The image below shows the correct plus sign symbol location to add a new pattern.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing
Add a new pattern and name each new pattern to record several within a file.

## Slide 16: Inputs
You can use inputs A–D to control a start and stop to a saved sequence.
Inputs A–D are connected to the input pins shown on the Lynxmotion SSC-32U board.
If no actual inputs are sensed or connected to the robot, you can select them in the FlowArm PLTW Software.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing
Notes: Note that pin A and B do not have a label.

## Slide 17: Inputs
Input A – Digital start sequence from beginning
Input B – Return from digital pause
Input C – Return from digital pause
Input D – Stop sequence in progress (e.g., emergency stop)
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 18: Inputs B and C
A pause in a step will halt the sequence at the beginning of a step.
Inputs B and C can be used to return motion to a sequence at a digital pause.
To add a digital pause to a step, use the procedure below.
Remove a pause using the same procedure.
1. Step Before
2. Toggle Pause
3. Step After
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 19: Inputs A and D
A signal from input A starts a sequence from the beginning or stops a sequence in progress, rewinds the sequence to home, and restarts the sequence.
A signal from input D will stop a sequence and is a good option for an emergency stop.
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 20: Input Response Summary
 | Sequence Status |  |  |  | 
Input | At Beginning | Stopped During | Stopped at End | At Digital Pause | In Progress
A | Starts from Beginning | Returns and Starts from Beginning | Returns and Starts from Beginning | Returns and Starts from Beginning | Stops and Restarts from Beginning
B | Starts from Beginning | Restarts from Current Time | Nothing | Resumes from Current Pause | Nothing
C | Starts from Beginning | Restarts from Current Time | Nothing | Resumes from Current Pause | Nothing
D | Nothing | Nothing | Nothing | Nothing | Stops at Current Time
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing

## Slide 21: Reference
AL5 arm guide. (2014). Retrieved January 1, 2016, from http://www.flowbotics.com/manuals/flowarm-pltw.pdf
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing