## Slide 1
Lynxmotion Robotic Arm
© 2016 Project Lead The Way, Inc.
Computer Integrated Manufacturing
http://www.lynxmotion.com/images

## Slide 2: Introduction
The AL5 series robotic arm is a five or six axis jointed arm-type robot driven by four to five servo motors. It uses a serial servo controller to control all motion.
http://www.lynxmotion.com/images
Notes: In Lesson 3.1 you learned about the different types of robots, their work envelopes, and their applications.

## Slide 3: Joints
Base
Shoulder
Elbow
Wrist
Wrist Rotate
http://www.lynxmotion.com/images
Gripper

## Slide 4: End Effector
An end effector is a device or tool connected to the end of a robot arm.
The Lynxmotion gripper is shown above.
http://www.lynxmotion.com/images
Notes: Other common types of end effectors are welders for cutting and joining operations, vacuum grippers for accurate pick and place operations, and sprayers for applications of sealers and paints.

## Slide 5: Work Envelope
The work envelope is spherical like the Scorbot and other jointed arm robots.

## Slide 6: Servos
Servos are electromechanical devices that use feedback to provide precise movement of the robot’s joints.
http://www.lynxmotion.com/images

## Slide 7: Servos: Wiring
Power is provided by the red and black wires.
Controller sends a pulse using the yellow wire to indicate which direction to turn and for how long.
http://www.lynxmotion.com/images

## Slide 8: Servos: Operation
SSC-32 sends a pulse to the servo motor on the yellow wire.
A pulse of 1.5msec moves the servo to its center position.
A pulse of 1msec moves the servo 360° counterclockwise, and a 2 msec pulse moves the servo 360° clockwise.
These values are approximate.
Notes: There are two versions of the Lynxmotion controller: SSC-32 and SSC-32U.
The SSC-32 uses a serial cable for communication between the controller and a computer.
The SSC-32U uses a USC cable for communication between the controller and a computer.

## Slide 9: Servos: Operation
SSC-32 controller moves each servo.
FlowArm software is the interface that makes complex moves easier to perform.

## Slide 10: SSC-32 Interface
SSC-32 is a serial servo controller that provides the interface between the robot and the computer.
It can be used to control up to 32 servos.

## Slide 11: Outputs: Servos
Pins 0-7 are reserved for robot servos.

## Slide 12: Outputs
Pins 8-15 are reserved for outputs and can be used to send information to other equipment.

## Slide 13: Inputs
Pins A-D are reserved for inputs and can be used to monitor switches and sensors.

## Slide 14: Servo Connections
Always check polarity when wires are attached to the SSC-32, and never attach wires while the board is powered on.
  Black servo wire to Ground
  Red servo wire to VS1 pin
  Yellow servo wire to PULSE pin
Notes: Unplug the unit from the wall and disconnect 9V battery before making any connections.

## Slide 15: Lynxmotion Robotic Arm Start Up and Shut Down Procedures
Refer to this resource for proper operation:
Lesson 3.3 Lynxmotion Robotic Arm Start Up and Shut Down Procedures
Notes: Lesson 3.3 Lynxmotion Robotic Arm Start Up and Shut Down Procedures is provided as a reference for proper use of the robotic arm.