AutoCAD Customization Instructions

William Hough High School

Drafting, Architecture & Engineering

Teacher: M. Mclean

Cornelius, NC

Charlotte-Mecklenburg Schools

February 3, 2014

Purpose of this Manual:

This manual is designed to provide instruction on how to customize the appearance and operation of

AutoCAD design software. These settings are required for all students enrolled in the Drafting program

at William Hough High School. The modifications are designed to provide more efficient operation, and a

darker background color that will prevent eye strain over extended periods of use.

Appearance Settings:

The following operations will be used to set the color scheme for AutoCAD.

1. Open AutoCAD from the Start Menu

2. Once AutoCAD is fully open; in the command window type: Options and press Enter.

The following window will appear:

3. Slide the Crosshair slider all the way to the right so that the crosshair size is 100%. (See above)

4. Left click on the Colors Button as shown in the screenshot

The following window should appear.

5. Set the color for the following listed items in the Context Menu to Black.

o 2D Model Space

o Sheet / Layout

o 3D Parallel Projection

o 3D Perspective Projection

o Plot Preview

Colors are selected from the color drop down menu at right as labeled below.

Once all colors have been set, select the Apply and Close button at the bottom of the page.

Once all colors have been set, select the Apply and Close button at the bottom of the page.

You should now be back to the Options Window as shown below:

Operation Settings:

6. From the Options Window, select the User Preferences tab as shown below, the left click on the

Right-Click Customization button.

The following window will appear:

7. Select the options indicated in the screenshot below; then select Apply & Close

You should now be back to the Options window. Select Apply; then select OK to close the Options

window.

8. In the command window, type OSNAP and press Enter. Setup your computer with checks in the

same boxes as shown.

9. Once you have completed adding checks in the spaces noted, select OK, and the OSNAP window

will close.

Select

Perpendicular and

Tangent only from

the right list

# Text boxes

Check all

boxes in

the left

list.

Select

Perpendicular and

Tangent only from

the right list

AUTOCAD

is now

setup for

use.

Repeat

Last

Command

ENTER

Shortcut

Menu

Set as

shown

here.

Left

Click

here

Context

Window

Should be set to

Uniform

Background for all

Color

Window –

Set each to

black.

Select

User

Preferences

Press the Right

Click

Customization

Button