William Hough High School

Cornelius, NC

Drafting 2 (Architecture)

Plan Criteria

Plan Name: “Savannah”

Drafting 2 (Architecture)

Unit 3.1.4 - The “Savannah” Project

September 24, 2012

Revised: February 16, 2014

Plan Criteria

Introduction:

The following criteria should be used in the creation of a new house plan…(The Savannah)

The Savannah plan should be drawn precisely as described in these notes, and according to the

drawings provided.

The Savannah is a (3) bedroom ranch style home with an open floor plan, and a medium

pitched roof. Front Hip or Gable roof details will be used to add variety, and to create a

distinctive look for your plans. Modifications should not be made to the rear or sides of the

house.

The following drawings should be turned in for full credit:

a. Title Sheet with square footage chart imported from Excel

b. Crawl Foundation

c. Slab Foundation

d. Floor Plan

e. Front Elevation

f.  Rear Elevation

g. Left Elevation

h. Right Elevation

i.  Roof Plan

j.  Side Load Garage Foundation & Floor Plan

k. Side Load Garage Elevations (Cutaway of Right Side and Front Only)

l.  Electrical Layout

m. Side Load Garage Electrical Layouts

Drawing Set Requirements:

1. All plans must be fully dimensioned and annotated.

2. Interior walls shall be dimensioned O.C. (On Center)

3. Dimensions should be pulled to the outside edge of exterior walls.

4. All Interior walls should be drawn with 4” thickness.

5. All Exterior walls are drawn with 4” thickness U.N.O. (Unless Noted Otherwise)

6. Walls with pocket doors must be drawn with 6” thickness to accommodate pocket door.

7. Plumbing walls must be drawn 6” thick to accommodate plumbing pipes

8. A side load garage option must be included in the drawing set.

a. A Full set of side load garage plans includes:

i. Foundation plan for side load garage

ii. Floor plan for side load garage

iii. A cutaway front elevation of the garage portion of the house

iv. A cutaway right side elevation of the garage portion of the house

Plan Criteria

Door Sizes and Types:

Garage Door (Overhead)                                 7’ x 16’Overhead Door (Front Facing)

Garage Door to Kitchen                                   2’- 8” (20 Minute Rated Steel - 6 Panel)

Front Entry Door                                              3/0 x 6/8 with 8” Sidelights & Transom

Master Bedroom                                              2/6 x 6/8 (6 Panel)

Bedroom2                                                        2/6 x 6/8 (6 Panel)

Bedroom3                                                        2/6 x 6/8 (6 Panel)

Bath2                                                                2/4 x 6/8 (6 Panel)

Linen Closet in Master Bath                             1/6 x 6/8 (6 Panel)

Master Bath

(Main Entry)                                            2/4 x 6/8 (6 Panel)

(Compartment Entry                               2/4 x 6/8 (6 Panel) (Pocket Door)

Walk-In Closet                                                   3’ Opening - (2) 1/6 x 6/8 Bi-Hinge Doors

Laundry Room                                                   5’-0” (2) 2’6” Bi-Fold Doors

Pantry                                                                1/6 x 6/8 (6 Panel)

Door to Patio                                                      2/8 x 6/8 Full View Door

Hall Closet                                                          2/4 x 6/8 (6 Panel)

Bedroom 2 Closet                                              2/4 x 6/8 (6 panel)

Bedroom 3 Closet                                             (2) 2/0 x 6/8 Bi-Hinge Doors (4’ Opening)

Plan Criteria

Window Size, Types & Locations:

Bedroom 3 		 (2) 2/8 x 5/0 Single Hung (Double)

Bedroom 2		 (1) 2/8 x 5/0 Single Hung

Master Bedroom	 (2) 2/8 x 5/0 Single Hung (Double)

Great Room 		 (3) 2/8 x 6/0 Single Hung

Garage 		 (3) 2/8 x 5/0 Single Hung

Kitchen 		 (1) 3/0 x 4/0 Casement (Above Sink)

Breakfast Area (2) 2/8 x 6/0 Single Hung (Double) (1 Set Rear Facing / 1 Set Side Facing)

Laundry Room (1) 2/0 x 4/0 Single Hung

Elevation Specifics:

Foundation Thickness:	 4”

Floor to Ceiling Height: 	 9’ 1-1/2”

Roof Pitch-

Front & Rear Elevations:	 8/12

Right & Left Elevations: 	 9/12

Overhang: 12”

Fascia Board:	            5 ½”

Frieze Board: 	            9 ¼”

Window Head Height:         7’- 6”

Door Head Height:              6’- 8”

Siding –

Hatch Angle: 	           315

Hatch Pattern: 	           ANSI-31

Plan Criteria

Electrical Guidelines:

General Electrical Notes: Should be placed beside floor plans on the electrical layer

Provide the following notes:

- 110V outlets to be placed on each bedroom wall no more than 6’ apart, and 18” above floor height. Place one outlet within 2’ of room entry door

- Provide a 110V outlet every 4’ at 12” above kitchen counters.

Garage (Side Load Garage should include the same items)

1 Waterproof Outlet located beside door to the kitchen

2 Overhead Lights in center of garage controlled by switch at kitchen door

1 Pre-wire for garage door openers (Push Button Switches)

1 Light on the left side of the garage door on the exterior of the house.

(Should be controlled by a switch at  entry to the kitchen).

Front Porch

1 Wall Mounted light beside door

1 weatherproof outlet

Great Room

1 Ceiling Fan controlled by 3 way switches located near front and back doors

(Provide a separate wire and switch for the fan and light)

1 “Half Hot” controlled by switch near front entry door

Kitchen

1 Overhead Light controlled by 3 way switches at garage entry & opening to Great Room

1 GFI beside Stove

1 Overhead light above sink controlled by switch beside sink

1 220 Volt outlet behind range

1 Switch controlling Sink Disposal

1 Switch controlling Dishwasher

Breakfast Room

1 Overhead light controlled by switch beside back door

(Light should be centered over table location)

Master Bedroom

1 Ceiling fan controlled by switch at entry door

(There should be a separate switch and wire for the fan and the fan light)

1 “Half Hot” on left wall.

(Locate roughly 4’ off rear wall. Control the half hot with a single switch by the door).

Secondary Bedrooms

1 Overhead light controlled by switch at entry door.

Walk-In Closet

1 Double Fluorescent light controlled by switch located on wall outside of closet door.

Hall Bath

1 Light over sink controlled by switch at door

1 Exhaust fan in center of ceiling controlled by switch at door

1 GFI at sink

Master Bath

1 Light over sink controlled by switch at door

1 Overhead Light between toilet and shower, controlled by a switch at pocket door entry

1 Exhaust fan in center of ceiling controlled by switch at door

1 GFCI beside sink

Rear Porch:

1 Wall mounted light (Jelly Jar)

1 weatherproof outlet

Foyer:

1 Overhead Light centered above door.

Laundry Room

1 220 Volt Outlet behind Dryer